CAN BUS :-INTERNALS:
## 1️⃣ CAN Frame Structure (Classical CAN)
Field	Size (bits)
Start of Frame (SOF)	1
Arbitration	11 or 29
Control	6
Data Length Code	4
Data Field	0-64 bits (0-8 bytes)
CRC	15 + 1 (CRC delimiter)
ACK	2
End of Frame (EOF)	7
Inter-frame space	~3

For Standard CAN (11-bit ID), a full 8-byte data frame is usually:
~111 bits total (with stuff bits excluded)
👉 But because of bit stuffing, usually we assume around 120 to 130 bits per frame in worst case.
## 2️⃣ Frame Transmission Time Formula
 Time BitsTransmission Time=BitrateTotal Bits​
At 1 Mbps (1,000,000 bits/sec):
If frame size ≈ 130 bits →
T=1,000,000130​=130μs
So one frame takes ~130 microseconds to transmit.
## 3️⃣ Frames per Second
 per secondFrames per second=1301,000,000​≈7,692frames/sec
So at maximum bus load, you can send around 7,600–7,700 full frames/sec.
## 4️⃣ Actual Data Throughput
Since data field is max 8 bytes = 64 bits:
 per secondPayload per second=7,692×8bytes≈61,500bytes/sec
So your actual data throughput is around ~60 KB/s, much less than 1 Mbps because of protocol overhead.
## 🔧 In Interviews — You Can Say:
At 1 Mbps, maximum theoretical payload is around 60–62 KB/s, due to protocol overhead, arbitration, bit stuffing, and inter-frame gaps.
# 🔥 CAN FD Frame Transmission Time Formula (Interview Hack)
Transmission Time ≈ Arbitration Time + Data Phase Time + Overhead
Let’s assume:
- Arbitration bitrate = 1 Mbps
- Data phase bitrate = 8 Mbps
Example:
64 bytes = 512 bits (data phase)
- Arbitration time ~50 bits (SOF + ID + control + CRC etc.)
- Data time = 512 / 8 Mbps = 64 µs
- Arbitration time = 50 / 1 Mbps = 50 µs
Total ≈ 50 µs + 64 µs = 114 µs per frame
👉 This formula impresses interviewers if you calculate roughly on the spot.
# 🔥 BONUS TIP: Golden Line to say in interview
"CAN FD improves bus utilization by increasing payload to 64 bytes and using dual-bit-rate phases, while maintaining backward compatibility with Classical CAN — which is why it's now widely used in modern automotive systems."
# 🚗 CAN Protocol Quick Sheet (Interview Ready)
## 🔧 Protocol Type
- Serial, Multi-Master, Message-Based, Broadcast
- ISO 11898 Standard
## 🔧 Why Message-Based?
- Data identified by Message ID (not node addresses)
- All nodes receive messages → filter based on ID
## 🔧 Bus Speed
Protocol	Max Bitrate
Classical CAN	1 Mbps
CAN FD	Arbitration: 1 Mbps Data Phase: up to 8 Mbps

## 🔧 Frame Structure (Classical CAN)
Field	Size
SOF	1 bit
Arbitration (ID)	11/29 bits
Control	6 bits
Data Length Code (DLC)	4 bits
Data	0–8 bytes
CRC	15 + 1 bits
ACK	2 bits
EOF	7 bits
Inter-frame space	~3 bits

## 🔧 CAN FD Differences
- Data: Up to 64 bytes
- BRS (Bit Rate Switch): Faster data phase
- CRC: 17/21 bits
- Stuff Bit Counter (less bit stuffing)
- Better bus utilization
## 🔧 Arbitration
- Lower ID = Higher priority
- Dominant bit (0) wins over recessive bit (1)
- Bitwise arbitration ensures collision-free bus
## 🔧 Bit Stuffing
- Insert opposite bit after 5 consecutive same bits
- Prevents clock drift
- Less stuffing in CAN FD due to Stuff Bit Counter
## 🔧 Error Handling
- CRC error
- Acknowledgement error
- Bit error
- Form error
- Stuff error
Automatic retransmission on error detection.
## 🔧 Common Applications
- Automotive (ECUs, airbags, ABS, powertrain, sensors)
- Industrial automation
- Medical devices
- Avionics
## 🔧 Advantages
- Reliable, real-time communication
- Multi-master support
- Priority-based arbitration
- Error detection & retransmission
- Easy to scale (add nodes without reconfig)
✅ Golden Interview Line:
"CAN ensures real-time, reliable, priority-based data transfer with error detection, while CAN FD extends this for high-bandwidth needs with larger payload and higher data phase speeds."
# 🔥 Bonus Formula
Frame Time = Arbitration Time + Data Phase Time + Overhead
- Classical CAN: ~130 µs per full 8-byte frame at 1 Mbps
- CAN FD: ~110 µs for 64-byte frame at arbitration 1 Mbps, data 8 Mbps

### 🔥 Trap 1:
Q: How many devices can be connected to CAN?
Wrong answer: Unlimited.
Correct answer:
- Theoretically many, practically limited by:
  - Bus load
  - Electrical characteristics
  - Propagation delay
  - Transceivers (typically 32 nodes per bus segment without repeater)
👉 In real automotive: usually 30–50 ECUs per bus.
### 🔥 Trap 3:
Q: Is CAN FD faster than Classical CAN?
Wrong answer: Yes, always.
Correct answer:
- Arbitration phase still at 1 Mbps.
- Only data phase can go up to 8 Mbps.
- So actual throughput depends on payload size.
### 🔥 Trap 6:
Q: Why bit stuffing is used?
Wrong answer: To separate frames.
Correct answer:
- For synchronization.
- Prevent long sequences of same bits which may desynchronize clock recovery circuits.